V. AREA OF OPERATION: PREFLIGHT PROCEDURES

NOTE: The examiner must select at least one TASK.

# A. TASK: PREFLIGHT INSPECTION (ASEL and ASES)

REFERENCES: AC 61-84; FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a preflight inspection, as applicable to the airplane used for the practical test, by describing—

  - reasons for the preflight inspection, items that should be inspected, and how defects are detected.

  - importance of using the appropriate checklist.

  - how to determine fuel and oil quantity and contamination.

  - detection of fuel, oil, and hydraulic leaks.

  - inspection of the oxygen system, including supply and proper operation (if applicable).

  - inspection of the flight controls and water rudder (if applicable).

  - detection of visible structural damage.

  - removal of tie-downs, control locks, and wheel chocks.

  - removal of ice and frost.

  - importance of the proper loading and securing of baggage, cargo, and equipment.

  - use of sound judgment in determining whether the airplane is airworthy and in condition for safe flight.

- Exhibits instructional knowledge of common errors related to a preflight inspection by describing—

  - failure to use or the improper use of checklist.

  - hazards which may result from allowing distractions to interrupt a visual inspection.

  - inability to recognize discrepancies to determine airworthiness.

  - failure to ensure servicing with the proper fuel and oil.

  - failure to ensure proper loading and securing of baggage, cargo, and equipment.

- Demonstrates and simultaneously explains a preflight inspection from an instructional standpoint.

# B. TASK: COCKPIT MANAGEMENT (ASEL and ASES)

REFERENCES: FAA-H-8083-3; FAA-S-8081-12; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of cockpit management by describing—

  - proper arranging and securing of essential materials and equipment in the cockpit.

  - proper use and/or adjustment of cockpit items such as safety belts, shoulder harnesses, rudder pedals, and seats.

  - occupant briefing on emergency procedures and use of safety belts.

  - proper utilization of all resources required to operate a flight safely: dispatchers, weather briefers, maintenance personnel, and air traffic control.

- Exhibits instructional knowledge of common errors related to cockpit management by describing—

  - failure to place and secure essential materials and equipment for easy access during flight.

  - failure to properly adjust cockpit items, such as safety belts, shoulder harnesses, rudder pedals, and seats.

  - failure to provide proper adjustment of equipment and controls.

  - failure to provide occupant briefing on emergency procedures and use of safety belts.

  - failure to utilize all resources required to operate a flight safely.

- Demonstrates and simultaneously explains cockpit management from an instructional standpoint.

# C. TASK: ENGINE STARTING (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23, FAA-H-8083-25; AC 91-13, AC 91-55; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of engine starting, as appropriate to the airplane used for the practical test, by describing—

  - safety precautions related to starting.

  - use of external power.

  - effect of atmospheric conditions on starting.

  - importance of following the appropriate checklist.

  - adjustment of engine controls during start.

  - prevention of airplane movement during and after start.

  - safety procedures for hand propping an airplane.

- Exhibits instructional knowledge of common errors related to engine starting by describing—

  - failure to properly use the appropriate checklist.

  - failure to use safety precautions related to starting.

  - improper adjustment of engine controls during start.

  - failure to assure proper clearance of the propeller.

- Demonstrates and simultaneously explains engine starting from an instructional standpoint.

# D. TASK: TAXIING—LANDPLANE (ASEL)

REFERENCES: FAA-H-8083-3; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of landplane taxiing by describing—

  - proper brake check and correct use of brakes.

  - compliance with airport/taxiway surface marking, signals, and ATC clearances or instructions.

  - how to control direction and speed.

  - flight control positioning for various wind conditions.

  - procedures used to avoid other aircraft and hazards.

- Exhibits instructional knowledge of common errors related to landplane taxiing by describing—

  - improper use of brakes.

  - improper positioning of the flight controls for various wind conditions.

  - hazards of taxiing too fast.

  - failure to comply with airport/taxiway surface marking, signals, and ATC clearances or instructions.

- Demonstrates and simultaneously explains landplane taxiing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to landplane taxiing.

# E. TASK: TAXIING—SEAPLANE (ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM; USCG Navigation Rules, International—Inland.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of seaplane taxiing by describing—

  - wind effect.

  - prevention of porpoising and skipping.

  - selection of the most suitable course for taxiing, following available marking aids.

  - conditions where idle, plowing, and step taxiing are used.

  - procedures for idle, plowing, and step taxiing.

  - control positioning for various wind conditions.

  - use of water rudders.

  - procedures used to avoid other aircraft and hazards.

  - procedures used to avoid excessive water spray into the propeller.

  - 180° and 360° turns in idle, plowing, and step positions.

  - application of right-of-way rules.

- Exhibits instructional knowledge of common errors related to seaplane taxiing by describing—

  - improper positioning of flight controls for various wind conditions.

  - improper control of speed and direction.

  - failure to prevent porpoising and skipping.

  - failure to use the most suitable course and available marking aids.

  - failure to use proper clearing procedures to avoid hazards.

  - failure to apply right-of-way rules.

- Demonstrates and simultaneously explains seaplane taxiing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to seaplane taxiing.

# F. TASK: SAILING (ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM; USCG Navigation Rules, International—Inland.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of sailing by describing—

  - procedures used in sailing (engine idling or shut down, as appropriate).

  - conditions and situations where sailing would be used.

  - selection of the most favorable course to follow.

  - use of flight controls, flaps, doors, and water rudders to follow the selected course.

  - procedures used to change direction from downwind to crosswind.

  - control of speed.

- Exhibits instructional knowledge of common errors related to sailing by describing—

  - failure to select the most favorable course to destination.

  - improper use of controls, flaps, and water rudders.

  - improper procedure when changing direction.

  - improper procedure for speed control.

- Demonstrates and simultaneously explains sailing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to sailing.

# G. TASK: BEFORE TAKEOFF CHECK (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of the before takeoff check by describing—

  - positioning the airplane with consideration for other aircraft, surface conditions, and wind.

  - division of attention inside and outside the cockpit.

  - importance of following the checklist and responding to each checklist item.

  - reasons for assuring suitable engine temperatures and pressures for run-up and takeoff.

  - method used to determine that airplane is in a safe operating condition.

  - importance of reviewing takeoff performance airspeeds, expected takeoff distances, and emergency procedures.

  - method used for assuring that the takeoff area or path is free of hazards.

  - method of avoiding runway incursions and ensuring no conflict with traffic prior to taxiing into takeoff position.

- Exhibits instructional knowledge of common errors related to the before takeoff check by describing—

  - failure to properly use the appropriate checklist.

  - improper positioning of the airplane.

  - improper acceptance of marginal engine performance.

  - an improper check of flight controls.

  - hazards of failure to review takeoff and emergency procedures.

  - failure to avoid runway incursions and to ensure no conflict with traffic prior to taxiing into takeoff position.

- Demonstrates and simultaneously explains a before takeoff check from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a before takeoff check.