VI. AREA OF OPERATION: AIRPORT AND SEAPLANE BASE OPERATIONS

NOTE: The examiner must select at least one TASK.

# A. TASK: RADIO COMMUNICATIONS AND ATC LIGHT SIGNALS (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-25; FAA-S-8081-12, FAA-S-8081-14; AIM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of radio communications and ATC light signals by describing—

  - selection and use of appropriate radio frequencies.

  - recommended procedure and phraseology for radio communications.

  - Receipt of, acknowledgement of, and compliance with ATC clearances and instructions.

  - interpretation of, and compliance with, ATC light signals.

- Exhibits instructional knowledge of common errors related to radio communications and ATC light signals by describing—

  - use of improper frequencies.

  - improper procedure and phraseology when using radio communications.

  - failure to acknowledge, or properly comply with, ATC clearances and instructions.

  - failure to understand, or to properly comply with, ATC light signals.

- Demonstrates and simultaneously explains radio communication procedures from an instructional standpoint.

- Analyzes and corrects simulated common errors related to radio communications and ATC light signals.

# B. TASK: TRAFFIC PATTERNS (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-25, AC 90-42, AC 90-66; FAA-S-8081-12, FAA-S-8081-14; AIM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of traffic patterns by describing—

  - operations at airports and seaplane bases with and without operating control towers.

  - adherence to traffic pattern procedures, instructions, and rules.

  - how to maintain proper spacing from other traffic.

  - how to maintain the desired ground track.

  - wind shear and wake turbulence avoidance procedures.

  - orientation with the runway or landing area in use.

  - how to establish a final approach at an appropriate distance from the runway or landing area.

  - use of checklist.

- Exhibits instructional knowledge of common errors related to traffic patterns by describing—

  - failure to comply with traffic pattern instructions, procedures, and rules.

  - improper correction for wind drift.

  - inadequate spacing from other traffic.

  - poor altitude or airspeed control.

- Demonstrates and simultaneously explains traffic patterns from an instructional standpoint.

- Analyzes and corrects simulated common errors related to traffic patterns.

# C. TASK: AIRPORT/SEAPLANE BASE, RUNWAY AND TAXIWAY SIGNS, MARKINGS, AND LIGHTING (ASEL and ASES)

REFERENCES: FAA-H-8083-23, FAA-H-8083-25; FAA-S-8081-12, FAA-S-8081-14; AIM; AC 150/5340-1, AC 150/5340-18.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of airport/seaplane base runway and taxiway signs, markings, and lighting by describing—

  - identification and proper interpretation of airport/seaplane base, runway and taxiway signs and markings with emphasis on runway incursion avoidance.

  - identification and proper interpretation of airport/seaplane base, runway and taxiway lighting with emphasis on runway incursion avoidance.

- Exhibits instructional knowledge of common errors related to airport/seaplane base, runway and taxiway signs, markings, and lighting by describing—

  - failure to comply with airport/seaplane base, runway and taxiway signs and markings.

  - failure to comply with airport/seaplane base, runway and taxiway lighting.

  - failure to use proper runway incursion avoidance procedures.

- Demonstrates and simultaneously explains airport/seaplane base, runway and taxiway signs, markings, and lighting from an instructional standpoint.

- Analyzes and corrects simulated common errors related to airport/seaplane base, runway and taxiway signs, markings, and lighting.