VII. AREA OF OPERATION: TAKEOFFS, LANDINGS, AND GO-AROUNDS

NOTE: The examiner must select at least two takeoff and two landing TASKS.

# A. TASK: NORMAL AND CROSSWIND TAKEOFF AND CLIMB (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a normal and crosswind takeoff and climb by describing—

  - procedures before taxiing onto the runway or takeoff area to ensure runway incursion avoidance.

  - normal and crosswind takeoff and lift-off procedures.

  - difference between a normal and a glassy-water takeoff (ASES).

  - proper climb attitude, power setting, and airspeed (VY).

  - proper use of checklist.

- Exhibits instructional knowledge of common errors related to a normal and crosswind takeoff and climb by describing—

  - improper runway incursion avoidance procedures.

  - improper use of controls during a normal or crosswind takeoff.

  - inappropriate lift-off procedures.

  - improper climb attitude, power setting, and airspeed (VY).

  - improper use of checklist.

- Demonstrates and simultaneously explains a normal or a crosswind takeoff and climb from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a normal or a crosswind takeoff and climb.

# B. TASK: SHORT-FIELD (CONFINED AREA—ASES) TAKEOFF AND MAXIMUM PERFORMANCE CLIMB (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a short-field takeoff and climb by describing—

  - procedures before taxiing onto the runway or takeoff area to ensure runway incursion avoidance.

  - short-field takeoff and lift-off procedures.

  - initial climb attitude and airspeed (VX) until obstacle is cleared (50 feet AGL).

  - proper use of checklist.

- Exhibits instructional knowledge of common errors related to a short-field takeoff and climb by describing—

  - improper runway incursion avoidance procedures.

  - improper use of controls during a short-field takeoff.

  - improper lift-off procedures.

  - improper initial climb attitude, power setting, and airspeed (VX) to clear obstacle.

  - improper use of checklist.

- Demonstrates and simultaneously explains a short-field takeoff and climb from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a short-field takeoff and climb.

# C. TASK: SOFT-FIELD TAKEOFF AND CLIMB (ASEL)

REFERENCES: FAA-H-8083-3; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a soft-field takeoff and climb by describing—

  - procedures before taxiing onto the runway or takeoff area to ensure runway incursion avoidance.

  - soft-field takeoff and lift-off procedures.

  - initial climb attitude and airspeed, depending on if an obstacle is present.

  - proper use of checklist.

- Exhibits instructional knowledge of common errors related to a soft-field takeoff and climb by describing—

  - improper runway incursion avoidance procedures.

  - improper use of controls during a soft-field takeoff.

  - improper lift-off procedures.

  - improper climb attitude, power setting, and airspeed (VY or VX).

  - improper use of checklist.

- Demonstrates and simultaneously explains a soft-field takeoff and climb from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a soft-field takeoff and climb.

# D. TASK: GLASSY-WATER TAKEOFF AND CLIMB (ASES)

REFERENCES: AC 91-69, FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a glassy-water takeoff and climb by describing—

  - procedures before taxiing onto the takeoff area to ensure waterway is clear of objects or obstructions.

  - flight control, flap, and water rudder use during glassy-water takeoff procedures.

  - appropriate planning attitude and lift-off procedures on glassy water.

  - initial climb attitude and airspeed (V, if an obstacle is present (50 feet AGL), or V).XY

  - proper use of after takeoff checklist.

- Exhibits instructional knowledge of common errors related to a glassy-water takeoff and climb by describing—

  - improper takeoff water way clearance procedures.

  - poor judgment in the selection of a suitable takeoff area.

  - improper use of controls during a glassy-water takeoff.

  - inappropriate lift-off procedures.

  - hazards of inadvertent contact with the water after becoming airborne.

  - improper climb attitude, power setting, and airspeed (VY or VX).

  - improper use of checklist.

- Demonstrates and simultaneously explains a glassy-water takeoff and climb from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a glassy-water takeoff and climb.

# E. TASK: ROUGH-WATER TAKEOFF AND CLIMB (ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a rough-water takeoff and climb by describing—

  - procedures before taxiing onto the takeoff area to ensure waterway is clear of objects or obstructions.

  - flight control, flap and water rudder use during rough-water takeoff procedures.

  - appropriate planning attitude and lift-off procedures on rough water.

  - initial climb attitude and airspeed (VX, if an obstacle is present (50 feet AGL), or VY).

  - proper use of after takeoff checklist.

- Exhibits instructional knowledge of common errors related to a rough-water takeoff and climb by describing—

  - improper takeoff water way clearance procedures.

  - poor judgment in the selection of a suitable takeoff area.

  - improper use of controls during a rough-water takeoff.

  - inappropriate lift-off procedures.

  - hazards of inadvertent contact with the water after becoming airborne.

  - improper climb attitude, power setting, and airspeed (VY or VX).

  - improper use of checklist.

- Demonstrates and simultaneously explains a rough-water takeoff and climb from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a rough-water takeoff and climb.

# F. TASK: NORMAL AND CROSSWIND APPROACH AND LANDING (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a normal and a crosswind approach and landing by describing—

  - how to determine landing performance and limitations.

  - configuration, power, and trim.

  - obstructions and other hazards which should be considered.

  - a stabilized approach at the recommended airspeed to the selected touchdown area.

  - course of action if selected touchdown area is going to be missed.

  - coordination of flight controls.

  - a precise ground track.

  - wind shear and wake turbulence avoidance procedures.

  - most suitable crosswind procedure.

  - timing, judgment, and control procedure during roundout and touchdown.

  - directional control after touchdown.

  - use of brakes (landplane).

  - use of checklist.

- Exhibits instructional knowledge of common errors related to a normal and a crosswind approach and landing by describing—

  - improper use of landing performance data and limitations.

  - failure to establish approach and landing configuration at appropriate time or in proper sequence.

  - failure to establish and maintain a stabilized approach.

  - inappropriate removal of hand from throttle.

  - improper procedure during roundout and touchdown.

  - poor directional control after touchdown.

  - improper use of brakes (ASEL).

- Demonstrates and simultaneously explains a normal or a crosswind approach and landing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a normal or crosswind approach and landing.

# G. TASK: SLIP TO A LANDING (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a slip (forward and side) to a landing by describing—

  - configuration, power, and trim.

  - obstructions and other hazards which should be considered.

  - a stabilized slip at the appropriate airspeed to the selected touchdown area.

  - possible airspeed indication errors.

  - proper application of flight controls.

  - a precise ground track.

  - wind shear and wake turbulence avoidance procedures.

  - timing, judgment, and control procedure during transition from slip to touchdown.

  - directional control after touchdown.

  - use of brakes (ASEL).

  - use of checklist.

- Exhibits instructional knowledge of common errors related to a slip (forward and side) to a landing by describing—

  - improper use of landing performance data and limitations.

  - failure to establish approach and landing configuration at appropriate time or in proper sequence.

  - failure to maintain a stabilized slip.

  - inappropriate removal of hand from throttle.

  - improper procedure during transition from the slip to the touchdown.

  - poor directional control after touchdown.

  - improper use of brakes (landplane).

- Demonstrates and simultaneously explains a forward or sideslip to a landing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a forward or sideslip to a landing.

# H. TASK: GO-AROUND/REJECTED LANDING (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a go-around/rejected landing by describing—

  - situations where a go-around/rejected landing is necessary.

  - importance of making a prompt decision.

  - importance of applying takeoff power immediately after the go-around/rejected landing decision is made.

  - importance of establishing proper pitch attitude.

  - wing flaps retraction.

  - use of trim.

  - landing gear retraction.

  - proper climb speed.

  - proper track and obstruction clearance.

  - use of checklist.

- Exhibits instructional knowledge of common errors related to a go-around/rejected landing by describing—

  - failure to recognize a situation where a go-around/rejected landing is necessary.

  - hazards of delaying a decision to go-around/rejected landing.

  - improper power application.

  - failure to control pitch attitude.

  - failure to compensate for torque effect.

  - improper trim procedure.

  - failure to maintain recommended airspeeds.

  - improper wing flaps or landing gear retraction procedure.

  - failure to maintain proper track during climb-out.

  - failure to remain well clear of obstructions and other traffic.

- Demonstrates and simultaneously explains a go-around/rejected landing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a go-around/rejected landing.

# I. TASK: SHORT-FIELD (CONFINED AREA—ASES) APPROACH AND LANDING (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a short-field approach and landing by describing—

  - how to determine landing performance and limitations.

  - configuration and trim.

  - proper use of pitch and power to maintain desired approach angle.

  - obstructions and other hazards which should be considered.

  - effect of wind.

  - selection of touchdown and go-around points.

  - a stabilized approach at the recommended airspeed to the selected touchdown point.

  - coordination of flight controls.

  - a precise ground track.

  - timing, judgment, and control procedure during roundout and touchdown.

  - directional control after touchdown.

  - use of brakes (ASEL).

  - use of checklist.

- Exhibits instructional knowledge of common errors related to a short-field approach and landing by describing—

  - improper use of landing performance data and limitations.

  - failure to establish approach and landing configuration at appropriate time or in proper sequence.

  - failure to establish and maintain a stabilized approach.

  - improper procedure in use of power, wing flaps, and trim.

  - inappropriate removal of hand from throttle.

  - improper procedure during roundout and touchdown.

  - poor directional control after touchdown.

  - improper use of brakes.

- Demonstrates and simultaneously explains a short-field approach and landing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a short-field approach and landing.

# J. TASK: SOFT-FIELD APPROACH AND LANDING (ASEL)

REFERENCES: FAA-H-8083-3; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a soft-field approach and landing by describing—

  - how to determine landing performance and limitations.

  - configuration and trim.

  - obstructions and other hazards which should be considered.

  - effect of wind and landing surface.

  - selection of a touchdown area.

  - a stabilized approach at the recommended airspeed to the selected touchdown point.

  - coordination of flight controls.

  - a precise ground track.

  - timing, judgment, and control procedure during roundout and touchdown.

  - touchdown in a nose-high pitch attitude at minimum safe airspeed.

  - proper use of power.

  - directional control after touchdown.

  - use of checklist.

- Exhibits instructional knowledge of common errors related to a soft-field approach and landing by describing—

  - improper use of landing performance data and limitations.

  - failure to establish approach and landing configuration at appropriate time or in proper sequence.

  - failure to establish and maintain a stabilized approach.

  - failure to consider the effect of wind and landing surface.

  - improper procedure in use of power, wing flaps, and trim.

  - inappropriate removal of hand from throttle.

  - improper procedure during roundout and touchdown.

  - failure to hold back elevator pressure after touchdown.

  - closing the throttle too soon after touchdown.

  - poor directional control after touchdown.

  - improper use of brakes.

- Demonstrates and simultaneously explains a soft-field approach and landing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a soft-field approach and landing.

# K. TASK: 180° POWER-OFF ACCURACY APPROACH AND LANDING (ASEL)

REFERENCES: FAA-H-8083-3; FAA-S-8081-12.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a 180° power-off accuracy approach and landing by describing—

  - configuration and trim.

  - effects of wind and selection of a touchdown area.

  - the key points in the pattern.

  - a stabilized approach at the recommended airspeed to the selected touchdown area.

  - coordination of flight controls.

  - timing, judgment, and control procedure during roundout and touchdown.

  - directional control after touchdown.

  - use of checklist.

- Exhibits instructional knowledge of common errors related to a 180° power-off accuracy approach and landing by describing—

  - failure to establish approach and landing configuration at proper time or in proper sequence.

  - failure to identify the key points in the pattern.

  - failure to establish and maintain a stabilized approach.

  - failure to consider the effect of wind and landing surface.

  - improper use of power, wing flaps, or trim.

  - improper procedure during roundout and touchdown.

  - failure to hold back elevator pressure after touchdown.

  - poor directional control after touchdown.

  - improper use of brakes.

- Demonstrates and simultaneously explains a 180° power-off accuracy approach and landing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a 180° power-off accuracy approach and landing.

# L. TASK: GLASSY-WATER APPROACH AND LANDING (ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a glassy-water approach and landing by describing—

  - how to determine landing performance and limitations.

  - configuration and trim.

  - deceptive characteristics of glassy water.

  - selection of a suitable landing area and go-around point.

  - terrain and obstructions which should be considered.

  - detection of hazards in the landing area such as shallow water, obstructions, or floating debris.

  - coordination of flight controls.

  - a precise ground track.

  - a power setting and pitch attitude that will result in the recommended airspeed and rate of descent throughout the final approach to touchdown.

  - how to maintain positive afterlanding control.

  - use of checklist.

- Exhibits instructional knowledge of common errors related to a glassy-water approach and landing by describing—

  - improper use of landing performance data and limitations.

  - failure to establish approach and landing configuration at appropriate time and in proper sequence.

  - failure to establish and maintain a stabilized approach at the recommended airspeed and rate of descent.

  - improper procedure in use of power, wing flaps, or trim.

  - inappropriate removal of hand from throttle.

  - failure to touch down with power in the proper stabilized attitude.

  - failure to maintain positive afterlanding control.

- Demonstrates and simultaneously explains a glassy-water approach and landing from an instructional standpoint.

- Analyzes and corrects simulated common errors related to a glassy-water approach and landing.

# M. TASK: ROUGH-WATER APPROACH AND LANDING (ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-23; FAA-S-8081-12, FAA-S-8081-14; POH/AFM.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of a rough-water approach and landing by describing—

  - how to determine landing performance and limitations.

  - review of wind conditions.

  - how landing area characteristics can be evaluated.

  - selection of a suitable landing area and go-around point.

  - terrain and obstructions which should be considered.

  - detection of hazards in the landing area such as shallow water, obstructions, or floating debris.

  - configuration and trim.

  - coordination of flight controls.

  - a precise ground track.

  - a stabilized approach at the recommended airspeed to the selected touchdown area.

  - timing, judgment, and control procedure during roundout and touchdown.

  - maintenance of positive after-landing control.

  - use of checklist.

- Exhibits instructional knowledge of common errors related to a rough-water approach and landing by describing—

  - improper use of landing performance data and limitations.

  - failure to establish approach and landing configuration at appropriate time or in proper sequence.

  - failure to establish and maintain a stabilized approach.

  - improper procedure in use of power, wing flaps, or trim.

  - inappropriate removal of hand from throttle.

  - improper procedure during roundout and touchdown.

  - failure to maintain positive after-landing control.

- Demonstrates and simultaneously explains a rough-water approach and landing from an instructional standpoint.

- Analyzes and corrects simulated common errors related a rough-water approach and landing.