XII. AREA OF OPERATION: BASIC INSTRUMENT MANEUVERS

NOTE: The examiner must select at least one TASK.

# A. TASK: STRAIGHT-AND-LEVEL FLIGHT (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-15; FAA-S-8081-14.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of straight-and-level flight solely by reference to instruments by describing—

  - instrument cross-check, instrument interpretation, and aircraft control.

  - instruments used for pitch, bank, and power control, and how those instruments are used to maintain altitude, heading, and airspeed.

  - trim procedure.

- Exhibits instructional knowledge of common errors related to straight-and-level flight solely by reference to instruments by describing—

  - “fixation,” “omission,” and “emphasis” errors during instrument cross-check.

  - improper instrument interpretation.

  - improper control applications.

  - failure to establish proper pitch, bank, or power adjustments during altitude, heading, or airspeed corrections.

  - faulty trim procedure.

- Demonstrates and simultaneously explains straight-and-level flight, solely by reference to instruments, from an instructional standpoint.

- Analyzes and corrects simulated common errors related to straight-and-level flight, solely by reference to instruments.

# B. TASK: CONSTANT AIRSPEED CLIMBS (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-15; FAA-S-8081-14.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of straight and turning, constant airspeed climbs, solely by reference to instruments by describing—

  - instrument cross-check, instrument interpretation, and aircraft control.

  - instruments used for pitch, bank, and power control during entry, during the climb, and during level off, and how those instruments are used to maintain climb heading and airspeed.

  - trim procedure.

- Exhibits instructional knowledge of common errors related to straight and turning, constant airspeed climbs, solely by reference to instruments by describing—

  - “fixation,” “omission,” and “emphasis” errors during instrument cross-check.

  - improper instrument interpretation.

  - improper control applications.

  - failure to establish proper pitch, bank, or power adjustments during heading and airspeed corrections.

  - improper entry or level-off procedure.

  - faulty trim procedure.

- Demonstrates and simultaneously explains a straight and turning, constant airspeed climb, solely by reference to instruments, from an instructional standpoint.

- Analyzes and corrects simulated common errors related to straight and turning, constant airspeed climbs, solely by reference to instruments.

# C. TASK: CONSTANT AIRSPEED DESCENTS (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-15; FAA-S-8081-14.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of straight and turning, constant airspeed descents, solely by reference to instruments by describing—

  - instrument cross-check, instrument interpretation, and aircraft control.

  - instruments used for pitch, bank, and power control during entry, during the descent, and during level off, and how those instruments are used to maintain descent heading and airspeed.

  - trim procedure.

- Exhibits instructional knowledge of common errors related to straight and turning, constant airspeed descents, solely by reference to instruments by describing—

  - “fixation,” “omission,” and “emphasis” errors during instrument cross-check.

  - improper instrument interpretation.

  - improper control applications.

  - failure to establish proper pitch, bank, or power adjustments during heading and airspeed corrections.

  - improper entry or level-off procedure.

  - faulty trim procedure.

- Demonstrates and simultaneously explains a straight and turning, constant airspeed descent, solely by reference to instruments, from an instructional standpoint.

- Analyzes and corrects simulated common errors related to straight and turning, constant airspeed descents, solely by reference to instruments.

# D. TASK: TURNS TO HEADINGS (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-15; FAA-S-8081-14.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of turns to headings, solely by reference to instruments by describing—

  - instrument cross-check, instrument interpretation, and aircraft control.

  - instruments used for pitch, bank, and power control during turn entry, during the turn, and during the turn rollout, and how those instruments are used.

  - trim procedure.

- Exhibits instructional knowledge of common errors related to turns to headings, solely by reference to instruments by describing—

  - “fixation,” “omission,” and “emphasis” errors during instrument cross-check.

  - improper instrument interpretation.

  - improper control applications.

  - failure to establish proper pitch, bank, and power adjustments during altitude, bank, and airspeed corrections.

  - improper entry or rollout procedure.

  - faulty trim procedure.

- Demonstrates and simultaneously explains a turn to a heading, solely by reference to instruments, from an instructional standpoint.

- Analyzes and corrects simulated common errors related to turns to headings, solely by reference to instruments.

# E. TASK: RECOVERY FROM UNUSUAL FLIGHT ATTITUDES (ASEL and ASES)

REFERENCES: FAA-H-8083-3, FAA-H-8083-15; FAA-S-8081-14.

Objective. To determine that the applicant:

- Exhibits instructional knowledge of the elements of recovery from unusual flight attitudes by describing—

  - conditions and situations that may result in unusual flight attitudes.

  - the two basic unusual flight attitudes—nose-high (climbing turn) and nose-low (diving spiral).

  - how unusual flight attitudes are recognized.

  - control sequence for recovery from a nose-high attitude and the reasons for that sequence.

  - control sequence for recovery from a nose-low attitude and the reasons for that sequence.

  - reasons why the controls should be coordinated during unusual flight attitude recoveries.

- Exhibits instructional knowledge of common errors related to recovery from unusual flight attitudes by describing—

  - failure to recognize an unusual flight attitude.

  - consequences of attempting to recover from an unusual flight attitude by “feel” rather than by instrument indications.

  - inappropriate control applications during recovery.

  - failure to recognize from instrument indications when the airplane is passing through a level flight attitude.

- Demonstrates and simultaneously explains a recovery from nose-high and a nose-low flight attitude from an instructional standpoint.

- Analyzes and corrects simulated common errors related to recovery from unusual flight attitudes.