# HOLDING PROCEDURES

Objective:

To teach the student the proper procedures and technique for piloting an airplane into and maintaining a holding pattern.

Content:

- Holding Components and Procedures

  - Setting of aircraft navigation equipment

  - Establishing the appropriate holding airspeed for the aircraft and altitude

  - Arriving at the holding fix and entry into the holding pattern

    - Direct Entry

    - Parallel Entry

    - Teardrop Entry

    - Timing procedure

    - Correction for wind drift

- Common Errors

  - Incorrect setting of aircraft navigation equipment

  - Inappropriate altitude, airspeed and bank control

  - Improper timing

  - Improper wind drift correction

  - Failure to recognize holding fix passage

  - Failure to comply with ATC instructions

References:

14 CFR Part 91, AIM

Aviation Instructor's Handbook, FAA-H-8083-9

Instrument Flying Handbook, FAA-H-8083-15

Instrument Rating ACS

Completion Standards:

The lesson is complete when the student can accurately perform the steps involved in entering into and maintaining a holding pattern using the materials covered in this lesson to the satisfaction of the instructor.

Instructors Notes:

- Holding components and procedures

  - Setting of aircraft navigation equipment

    - Record/readback holding clearance, including fix

    - Tune appropriate NAVAID(s) to indentify holding fix

      - VOR (After reaching fix twist OBS to inbound course)

      - NDB

      - Intersection (e.g., 2 VOR radials)

        - Two VOR receivers

          - Tune one to VOR radial defining course to holding fix

          - Tune the other to VOR radial (FROM indication) defining intersection holding fix

        - Only one VOR recevier

          - Alternately tune each VOR

          - Tune to VOR radial defining course to fix

          - Established on course to fix, tune to VOR radial FROM that defines intersection

          - In hold, turning inbound, tune to VOR radial defining inbound leg

          - Established on inbound leg, tune to VOR radial FROM that indentifies intersection holding fix

      - DME

      - GPS/RNAV

  - Requirement for establishing the appropriate holding airspeed for the aircraft and altitude

    - Begin airspeed reduction to holding airspeed within 3 minutes prior to arriving at fix

    - Recommend approach airspeed, e.g., C-TR182, 100 KIAS

    - Standard maximum holding speeds

      - 265 KIAS > 14,000 ft

      - 230 KIAS 6,001 - 14,000 ft

      - 200 KIAS MHA - 6,000 ft

    - IFR chart icons depict nonstandard holding airspeeds

Use HI to plan holding pattern entry:

  - Recognition of arrival at the holding fix and the prompt initiation of entry into the holding pattern

    - Arrival at holding fix indicated by station passage (VOR, NDB), or arrival at intersection or waypoint (GPS/RNAV)

    - FAA recommends direct, parallel or teardrop entry into the hold

      - Direct - upon arrival at fix from DIRECT ENTRY sector (see image below), turn to follow the holding pattern

      - Parallel - upon arrival at fix from PARALLEL ENTRY sector, turn to a heading parallel to holding course outbound on nonholding side for pproximately 1 minute, then turn more than 180° in direction of holding pattern and return direct to holding fix or intercept inbound course

      - Teardrop - upon arrival at fix from TEARDROP ENTRY sector, turn outbound to a heading of 30° on holding side of inbound leg for approximately 1 minute, then turn in the direction of the holding pattern to intercept the inbound course

      - Timing procedure

        - Standard inbound leg duration

          - 1½ minutes > 14,000 ft

          - 1 minute < 14,000 ft

        - Start outbound timing

          - VOR: reversal of TO/FROM indicator

          - Intersection: wings level after turn from fix

          - NDB: abeam fix (RB to fix = 90 or 270° +/- WCA)

          - DME: wings level after turn from fix

        - Outbound leg duration

          - Apply 2 x (inbound time deviation) for relatively small deviations (< 30 seconds)

          - Apply ½ - 1 x (inbound time deviation) for large deviations

      - Correction for wind drift

        - Determine inbound wind correction angle (WCA)

        - Apply 3 x WCA outbound for relatively small WCA (<15°)

        - Apply 2 x WCA outbound for large WCA

      - Use of DME in a holding pattern

        - DME distance defines holding fix

        - ATC specifies length of outbound leg

        - Turn inbound when DME indicates outbound leg completed

      - Compliance with ATC reporting requirements

        - Report time and altitude reaching holding fix ("entering hold")

        - Report leaving holding fix

- Common Errors

  - Incorrect setting of aircraft navigation equipment

Visualize/draw hold to aid positional awareness

  - Inappropriate altitude, airspeed and bank control

Standard rate turns

  - Improper timing

  - Improper wind drift correction

  - Failure to recognize holding fix passage

Include navigation instruments in scan

  - Failure to comply with ATC instructions

Request clarification if uncertain