# RADIO COMMUNICATIONS AND ATC LIGHT SIGNALS (ASEL and ASES)

Objective:

To familiarize the student with radio communications procedures. To familiarize the student with ATC light-gun signals and their meanings.

Note: Before this lesson the student should read the AIM’s Pilot/Controller Glossary and AIM Chapter 4.

Review communications requirements for different airspace areas

Content:

- Radio License

- Radio equipment

  - VHF 720: 118.0 – 135.975 KHz

  - VHF 760: 118.0 – 136.975 KHz

  - Line-of-sight

- Discuss Phonetic alphabet AIM C. 4-2-7

- Discuss communication examples AIM C. 4

- Discuss hand signals AIM C. 4-2-25

- Discuss Light-gun signals

- Discuss lost communication procedures appropriate to student level

Things to Avoid (Common Errors):

- Use of improper frequencies

- Improper procedure and phraseology for radio communications

- Failure to acknowledge or properly comply with, ATC clearances and instructions

- Failure to understand or properly comply with ATC light signals

References:

Pilot’s Handbook of Aeronautical Knowledge – Chapter 12

Completion Standards:

The lesson is complete when the instructor determines that the student has adequate knowledge of radio communications and ATC light-gun signals by giving an oral or written exam.

Instructor Notes:

- Selection and Use of Appropriate Frequencies

  - Preflight Planning

    - Always plan ahead as to frequencies needed

    - Look up the frequencies of all the facilities you might use and/or need during the flight

      - This information can be found in the AFD, Sectional Charts, etc.

      - Ground is always 121 point something

    - Put all this information in your Nav Log, preferably in the order you will use it to make things easy

  - During Flight frequencies may need to be found - keep organized and find them before they’re needed

    - Know who you are calling

  - The AFD contains all pertinent frequencies within/around the airport(s) you are operating in

    - Weather, Tower/CTAF, Clearance Del, Ground, Unicom, Navaids, FSS, Approach/Departure

  - Charts provide frequencies as you navigate

    - Communications Boxes (FSS)

    - Airport data lists tower/CTAF, Unicom, weather frequencies

    - VOR frequencies are shown in blue outlined boxes

      - HIWAS, TWEB, ASOS/AWOS available on some VORs

    - Class B, C, TRSA, and some radar approach frequencies are provided below Tower frequencies/info

  - After in contact with controllers, frequencies will be provided to reach further controllers

  - CE - Use of improper frequencies

    - Caused by inadequate planning, misreading frequencies, or mistuning the radio

    - Double check and read out loud frequencies also repeat frequencies when advised to change

    - Monitor the frequency before transmitting

- Procedure and Phraseology for Radio Communications

  - Understanding is the single most important thought in pilot-controller communications

    - It is essential that pilots acknowledge each radio call with ATC with the appropriate aircraft call sign

    - Brevity is important, but if necessary use whatever words will get your message across

    - Good phraseology enhances safety and is the mark of a professional pilot

      - Pilot/Controller Glossary is very helpful in learning what certain words/phrases mean (AIM)

  - Radio Technique

    - LISTEN before you transmit

    - THINK before transmitting - Know what you want to say before you say it (write it down if needed)

    - After transmitting, wait a few seconds before calling again (The controller may be busy)

    - Be alert to the sound/lack of sounds in the receiver

      - Check your volume, frequency, and make sure the microphone isn’t stuck on transmit

    - Be sure you are within the performance range of your equipment and the ground station equipment

      - Remember higher altitudes increase the range of VHF “line of sight” communications

  - Radio calls can be broken down into:

    - Whom you are calling

    - Who you are

    - Where you are

    - What you want to do

  - CE - Improper procedure and phraseology for radio communications

    - Think before you transmit and understand the controller may be busy

    - Tailor your calls to match the controller’s workload

- ATC Clearances and Instructions

  - Acknowledge all ATC clearances by repeating key points followed by your call sign

    - You must read back all hold short instructions

    - Always repeat altitudes and headings

    - When advised to change frequencies acknowledge the instruction and change ASAP

  - If a clearance is blocked or not understood, do not guess/ignore, ask the controller to “Say Again”

  - Once you, the PIC, obtain an ATC clearance you cannot deviate from it unless in an emergency (91.123)

    - If you cannot accept a clearance from ATC advise them of the reason and obtain a new clearance

  - The PIC is directly responsible for, and the final authority to the operation of the airplane

    - Obtain proper clarification on any clearance not understood or that would create a bad situation

  - CE – Failure to acknowledge or properly comply with, ATC clearances and instructions

    - Ask the controller to repeat if you did not understand the message

    - Learn to divide attention in order to properly hear and comply with all messages

- ATC Light Signals

  - Arriving Aircraft

    - Transmitter Failure - Receive no response to calls, and receive calls but none directed to you

      - Determine the direction and flow of aircraft, enter the pattern and look for light signals

      - Acknowledge light signals by rocking wings during the day and flashing lights at night

      - After landing, call the tower to advise them of the situation

    - Receiver Failure - Receiving no calls on tower/ATIS frequencies

      - Transmit to the tower your position, situation, intention to land

      - Use the same procedures as above

  - Departing Aircraft

    - Attempt to fix any radio failure before leaving, if it can’t be fixed call tower by phone and request to depart without two way communications

    - If authorized, you will get departure info and requested to monitor tower/watch for light signals

    - During daylight, acknowledge transmissions/ signals by promptly executing the action requested

      - Rock wings/blink lights as well

    - If the radio fails after departing the ramp, watch for light signals/monitor ground and return

  - CE - Failure to understand or properly comply with ATC light signals

    - Know the light signals and their meanings

    - Practice light signals if possible