# STEEP TURNS (ASEL and ASES)

Objective:

To develop the smoothness, coordination, orientation, division of attention, and control techniques necessary for the execution of maximum performance turns when the airplane is near its performance limits.

Before Flight:

  - 45-60° bank angle

  - Airspeed at or below VA

  - 360* minimum

  - An aircraft’s max performance turns limited by:

  - Power output

  - Limit load factor

  - Aerodynamic characteristics

  - Stall speed increases with the square of the load factor

Maneuver Elements:

- Clear the area

- Choose forced landing area

- Configure aircraft: straight-and-level, airspeed less than VA, altitude ≥1600’ AGL

- Select outside references

- Establish bank between 45º – 60º and simultaneously apply back elevator pressure and add power (C172RG: trim up 2 half-turns and 23” Hg, 2300 RPM) to maintain altitude ± 100’ (stay above 1500’) (50º for commercial maneuvers, 45º for private maneuvers)

- Trim as needed

- Keep ball centered

- Use external references: horizon for bank while also looking for traffic

- Anticipate roll-out by leading approx. 20º (half bank angle) to original heading ± 10º

- Upon completion of 360º turn (usually left), complete a second 360º to the opposite direction (usually right); a perfect turn will end with slight turbulence as you hit your own wake

- Adjust pitch, power, trim as necessary

- Maintain ball centered

- Look for traffic

Aircraft Setup:

Flaps up, gear up

Va: (C172RG: 18” Hg, 2300 RPM, 106 KIAS at MGW)

Things to Avoid (Common Errors):

- Failure to clear area

- Excessive pitch change during entry or recovery

- Starting recovery prematurely

- Failure to stop the turn on a precise heading

- Excessive rudder during recovery, resulting in skidding

- Inadequate power management

- Poor coordination

- Gaining altitude in right turns or losing altitude in left turns

- Failure to maintain a constant bank angle

- Disorientation

- Attempting to perform maneuver by instrument reference instead of visual

- Failure to scan for traffic during the maneuver

Diagrams:

References:

Airplane Flying Handbook – Chapter 9

Completion Standards:

The lesson is complete when the student demonstrates knowledge through a written or oral exam and is able to perform steep turns to the satisfaction of the instructor and in accordance with the current Practical Test Standards for the student’s stage of training.